## Slide 1: WG4-影像(Image)聯測

## Slide 2: WG4影像(Image)目標對象
醫院資訊系統(HIS)
影像傳輸與管理系統(PACS)
儀器製造商
新創與醫學影像AI公司
造影儀器商(影像產生者)
影像檢視
醫療機構資訊室
學術機構
Freelancer

## Slide 3: WG4聯測範圍
DICOM Part 18: Studies Service and Resources
FHIR ImagingStudy
FHIR Observation
DICOM Query/Retrieve (Optional)

## Slide 4: WG4聯測項目與規格
  查詢影像與標記 (Query)
    DICOM Query: C-FIND (Optional - 待討論)
    DICOMWeb: QIDO階層式查詢 – Studies-Series-Instances
    FHIR ImagingStudy
    FHIR observation SVG annotation
調閱影像與標記 (Retrieve)
    DICOM Retrieve C-MOVE (Optional - 待討論)
    DICOMWeb: WADO-RS
    DICOMWeb: WADO-URI
    FHIR Observation SVG annotation
  影像與標記顯示一致性

## Slide 5: 測試格式
Query:
  DICOMWeb QIDO - DICOM JSON
  DICOM C-FIND: DICOM
  FHIR JSON
    Imaging Study
    FHIR Observation SVG annotation
Retrieve:
  DICOMWeb : DICOM, JPEG
  DICOM C-MOVE: DICOM
  JSON: FHIR Observation SVG annotation

## Slide 6: 測試Transfer Syntax -無壓縮
Transfer Syntax UID | Transfer Syntax name
1.2.840.10008.1.2 | Implicit VR Endian: (Default Transfer Syntax for DICOM)
1.2.840.10008.1.2.1 | Explicit VR Little Endian
1.2.840.10008.1.2.2 | Explicit VR Big Endian

## Slide 7: 測試Transfer Syntax -影像壓縮
Transfer Syntax UID | Transfer Syntax name
1.2.840.10008.1.2.4.50 | JPEG Baseline (Process 1): Default Transfer Syntax for Lossy JPEG 8-bit Image Compression
1.2.840.10008.1.2.4.51 | JPEG Baseline (Processes 2 & 4): Default Transfer Syntax for Lossy JPEG 12-bit Image Compression (Process 4 only)
1.2.840.10008.1.2.4.70 | JPEG Lossless, Nonhierarchical, First- Order Prediction (Processes 14 [Selection Value 1]): Default Transfer Syntax for Lossless JPEG Image Compression
1.2.840.10008.1.2.4.80 | JPEG-LS Lossless Image Compression
1.2.840.10008.1.2.4.81 | JPEG-LS Lossy (Near- Lossless) Image Compression
1.2.840.10008.1.2.4.90 | JPEG 2000 Image Compression (Lossless Only)
1.2.840.10008.1.2.5 | RLE Lossless

## Slide 8: 測試SOP Class -標記
Transfer Syntax UID | Transfer Syntax name
1.2.840.10008.5.1.4.1.1.1 | CR Image Storage
1.2.840.10008.5.1.4.1.1.1.1 | Digital X-Ray Image Storage – for Presentation
1.2.840.10008.5.1.4.1.1.1.2 | Digital Mammography X-Ray Image Storage – for Presentation
1.2.840.10008.5.1.4.1.1.1.3 | Digital Intra – oral X-Ray Image Storage – for Presentation
1.2.840.10008.5.1.4.1.1.104.1 | Encapsulated PDF Storage
1.2.840.10008.5.1.4.1.1.12.1 | X-Ray Angiographic Image Storage
1.2.840.10008.5.1.4.1.1.129 | Standalone Positron Emission Tomography Curve Storage
1.2.840.10008.5.1.4.1.1.2 | CT Image Storage
1.2.840.10008.5.1.4.1.1.3 | Ultrasound Multiframe Image Storage
1.2.840.10008.5.1.4.1.1.4 | MR Image Storage
1.2.840.10008.5.1.4.1.1.6.1 | Ultrasound Image Storage

## Slide 9: 測試SOP Class -影像壓縮
Transfer Syntax UID | Transfer Syntax name
1.2.840.10008.5.1.4.1.1.11.1 | Grayscale Softcopy Presentation State Storage SOP Class
1.2.840.10008.5.1.4.1.1.481.3 | Radiation Therapy Structure Set Storage
1.2.840.10008.5.1.4.1.1.66.4 | Segmentation Storage
Embedded in Image | DICOM Overlay
 | FHIR Observation SVG annotation

## Slide 10: WG4聯測規劃情境
測試情境1: 傳統DICOM Q/R (待討論)
  使用傳統DICOM Network查詢與調閱影像與標記
測試情境2: Web Access
  使用DICOMWeb階層式查詢方式查詢DICOMWeb主機，並依照DICOM階層式架構回傳結果
  調閱使用WADO-URI或WADO-RS
測試情境3: Integration with FHIR
  查詢FHIR ImagingStudy Resources
  使用WADO-URI或WADO-RS調閱影像以及標記
  或使用FHIR REST API調閱FHIR Observation SVG annotation

## Slide 11: WG4連測督察員招募
連測督察員(Monitor)資格
  領域專家(Domain Expert)以及開發IHE Domain專家
  非受雇於連測參加的機構(廠商)
  IT 管理者具備技術背景以及具有系統整合實務經驗
  熟悉IHE Integration Profiles 以及標準
  對於協助工程師解決問題有興趣
領域
  標準專家: IHE DICOM, FHIR
責任與工作
  需全程參與 (2.5天)
  協助聯測團隊排除問題
  使用工具或自我專業知識提供驗證與測試結果
督察員招募
  醫院、工程師、學術單位、志工
  提供交通、住宿以及餐費

## Slide 12
簡報結束，謝謝聆聽
cylien.dicom@gmail.com
We are DICOM & IHE Compatible
  MISAT 2020- WG4 - 影像聯測工作小組
  WG4 Image LINE群組：https://line.me/R/ti/g/SlZRPemBiL
  Mail list: misat_wg4@googlegroups.com
  徵求聯測測試影像：上傳至: http://upload2020.dicom.org.tw